## Slide 1: Cluster Tracker
Group 4
Ryan Tang Li Yen
Goh Kheng Xi, Jevan
Lock Mei Lin

## Slide 2: Content
Aim and outcomes
Mechanical assembly
Operational flow
IWR6843 (mmWave)
L515 (3D camera)
Conclusion

## Slide 3
Aim
To enforce social-distancing rules by identifying and tracking clusters of people – cluster size, inter-cluster distance, and inter-cluster interactions – through sensor fusion (radar and LiDAR camera).

## Slide 4: Outcome
Responsibilities
Ryan Tang : Jetson Nano, mechanical and electronic assemblies
Jevan Goh : mmWave sensor, machine learning algorithms
Mei Lin : LiDAR camera, machine learning algorithms
1. Able to detect and track people from each sensor
2. Able to share data between sensors in real-time for better tracking accuracy
3. Able to measure distances between people and signal for violation

## Slide 5
Server (Host PC)
UART
COMPort
Parsing of data
If new target, send location to Jetson Nano
Request for data (violations from child script)
Jetson Nano
Paramiko
Servo Control Script
Start servo
COMPort
Human detection
Distance measuring
Check for violation and send back to main script
Visual output
IWR6843
Read point cloud data
Servo Motor
Pans L515 to location
L515
Reads RGBD
START
END
Server main script
L515 child script

## Slide 6: Mechanical Assembly
Intel RealSense L515 LiDAR Camera
IWR6843 AOP EVM mmWave Sensor
Host PC
Pan-tilt servo motors
Jetson Nano
PCA9685 PWM/Servo Driver
133 mm
61 mm
60 mm
91 mm
23 mm
Device | Power | Source
Servo Driver | 5 V 4 A | 4 x AA alkaline cells
L515 and mmWave | 5 V 0.5 A | Host PC USB port
Jetson Nano | 5 V 2 A | AC power adaptor
Power Consumption

## Slide 7: IWR6843 AOP EVM
Fast Modulated Continuous Waveform
60GHz (~4mm)
Range
Velocity and acceleration
Angle

## Slide 8: Algorithm (on-chip detection)
Fast-fourier transform
Static clutter removal
Beamforming
CFAR-CASO (Constant False Alarm Rate)
Elevation and doppler estimation

## Slide 9: Algorithm (on-chip tracking)
Point clouds tagging
Prediction (Extended Kalman Filter)
Association (DBSCAN - Mahalanobis distance)
Allocate
Update
Maintenance (Detect, Active, Static, Free)

## Slide 11: IWR6843 TLV (Server script)

## Slide 12: L515
Able to detect human
Able to count the number of people in a frame
Able to get distance
Able to detect people standing close together
Current state

## Slide 13: L515 depth data
Time-of-flight depth sensing 3D camera ​
​
Pixels in the depth image represents the distance
Dark red region is the furthest

## Slide 14: Object detection model
Locate the presence of human with a bounding box
Pretrained YOLOv5 model to detect the human class
Human detection done on the RGB image
Depth data obtained from the Depth image

## Slide 15: Distance between humans
YOLOv5 returns the 2D pixel coordinates of detected human
Deprojection: 2D pixel coordinates and corresponding depth value mapped to a 3D point location
3D x and z coordinates of the human used to calculate distance
If distance between humans is less than 1.5m, bounding box turns red
Notes: https://knowledge.autodesk.com/support/maya/learn-explore/caas/CloudHelp/cloudhelp/2015/ENU/Maya/files/Interface-overview-3D-coordinates-htm.html

## Slide 16: General specifications
FOV(horizontal) | 120 degrees
Range | 12m
Maximum velocity | 6m/s
Max number of targets | 13
Accuracy | 62%

## Slide 17: Thank You!